/* binary search only works if f(x) increases w.r.t of x
 * but in this problem, f(x) is unimodal
 * that is, at first, increasing x, f(x) increases, after a certain value, increasing x causes f(x) to decrease
 * | /	|
 * | /	|
 * | /	| ^
 * | /	| / \
 * | /	| / \
 * ^ | /	^	| / \
 * | | /	|	| / \
 * f(x)|-------------------	f(x) |------------------
 * x ->	x ->
 *
 * Binary Search Works Here	Ternary Search Works Here
 */

long double ternarySearch(long double lo, long double hi) {
long double l1, l2, ans;
for(int i = 0; i < 100; ++i) {
l1 = lo+(hi-lo)/3.0;
l2 = hi-(hi-lo)/3.0;
if(f(l1) > f(l2)) {	// Function f(x) generates output for input x
hi = l2;
ans = l1;
}
else
lo = l1;
}
return ans;
}

// Bisection Loop:
double Bisect(double lo, double hi) {
double ans, mid;
        for(register int i = 0; i < 50; i++) {
        mid = (lo+hi)/2.0;
        if(f(mid) <= EPS) { // As it returns double, for precision EPS is added instead of
        ans = mid;	// f(mid) == 0
        hi = mid;
        }
        else
        lo = mid;
        }
return ans;
}